## Slide 1: AE Hackathon AR.Drone 2.0 Workshop
11/5/16
Presenters: Evan Hammac, Zsolt Kira, Ph.D.

## Slide 2
Objectives of Workshop
Task: Make AR Drone track a detected tag
Getting Started:
  Download and Install Preconfigured Virtual Machine
  Fly AR.Drone Using Keyboard Controller on the Virtual Machine
Goals:
  Brief Overview of ROS and its Capabilities
  Demonstrate Capabilities of hacking code found on the Virtual Machine

## Slide 3
Downloading and Installing the Virtual Machine
First: Google “Up and flying with the AR drone and ROS”
  Link: http://robohub.org/up-and-flying-with-the-ar-drone-and-ros-getting-started/
The tutorials found here are detailed instructions for everything to do with installing and updating the virtual machine.
There is a catch however…

## Slide 4
Downloading and Installing the Virtual Machine
The tutorial has not been updated in quite some time and the link for the .ova file times out
Google “Mike Hamer github” and click the first link
Click the repository “ardrone_tutorials_getting_started”
Scroll down and click the hyperlink “virtual machine image”

## Slide 5
Downloading and Installing the Virtual Machine
This download is quite large
In the meantime let’s download VirtualBox
Once image file is downloaded refer back to “Up and Starting with AR drone…. Webpage”
Follow the steps and verify command and control of AR.drone
  The examples uses the Robot Operating System (ROS) framework
  To run: roslaunch ardrone_tutorials keyboard_controller.launch

## Slide 6
ROS Overview
Large number of robotics groups using Robot Operating System (ROS)
Like an OS, provides basic functionality used commonly in robotics
  Nodes ingest input data, process it, and push out data
  Messaging system (publish/subscribe) mechanism
  Transformations
  Logging and debugging
  Visualization of sensor data/robot
  Simulation
Lots of stacks built on top of this: Mapping, perception, planning, navigation, controls, drivers to hardware
Slides by Alec Poitzsch

## Slide 7: ROS: Reusable code!
PR2 Roomba Care-O-bot 3
Slides by Alec Poitzsch

## Slide 8: A meta-operating system for robots
Slides by Alec Poitzsch

## Slide 9: Comparison: the PC ecosystem
Standardized layers
System software abstracts hardware
Applications leverage other applications (such as database, web server).
Widely existent sets of libraries
Applications
Application building blocks
System software
Hardware
Slides by Alec Poitzsch

## Slide 10: Comparison: the robotics ecosystem
Applications
Application building blocks
System software
Hardware
Applications
ROS
Hardware
Slides by Alec Poitzsch

## Slide 11: What is ROS?
A “Meta” Operating System.
  Open source
  Runs in Linux (esp. Ubuntu)
  Ongoing Windows implementation
Agent based (nodes)
Message passing
  Publish
  Subscribe
  Services via remote invocation
Supports numerous programming languages (C++, Python, Lisp, Java)
Slides by Alec Poitzsch

## Slide 12: What is ROS?
Low level device abstraction
  Joystick
  GPS
  Camera
  Controllers
  Laser Scanners
  …
Application building blocks
  Coordinate system transforms
  Visualization tools
  Debugging tools
  Robust navigation stack (SLAM with loop closure)
  Arm path planning
  Object recognition
  ...
Application building blocks
System software
ROS
Slides by Alec Poitzsch

## Slide 13: What is ROS?
Software management (compiling, packaging)
Remote communication and control
Slides by Alec Poitzsch

## Slide 14: What is ROS?
Founded by Willow Garage
Exponential adoption
Countless commercial, hobby, and academic robots use ROS (http://wiki.ros.org/Robots)
Slides by Alec Poitzsch

## Slide 15: ROS Philosophical goals
“Hardware agnosticism”
Peer to peer
Tools based software design
Multiple language support (C++/Java/Python)
Lightweight: runs only at the edge of your modules
Free
Open source
Suitable for large scale research and industry
Slides by Alec Poitzsch

## Slide 16: Conceptual levels of design
16
Node 1
Laser Scanning
Node 2: Map Building
Node 3: Planning
(C) File-system level: ROS Tools for managing source code, build instructions, and message definitions.
Node 4
(B) Computation Graph: Peer-to-Peer Network of
ROS nodes (processes).
Node 5
Node 6
Node7
Carnegie Mellon
(A) ROS Community: ROS Distributions, Repositories
Slides by Alec Poitzsch
Notes: (A) Community Level: Resources that enable separate communities to exchange software: (i) ROS Distributions (ii) Code Repositories (Willow Garage, MIT) (iii) Wiki (B) Computation Graph Level: Peer-to-Peer network of ROS processing that are processing sensor data and doing other computations. Nodes can be distributed across machines (C) Filesystem Level: Ros has lots of tools for (i) organizing source code (ii) simplifying build instructions / dependencies (iii) Managing message definitions

## Slide 17: Tools-based software design
Tools for:
Building ROS nodes
Running ROS nodes
Viewing network topology
Monitoring network traffic
Many cooperating processes, instead of a single monolithic program.
Slides by Alec Poitzsch
Notes: (A) No Monolithic Runtime Environment (B) Small tools for building + running ros nodes: visualizing network topology, measuring bandwidth utilization, plotting.

## Slide 18: Multiple language support
ROS is implemented natively in each language.
Quickly define messages in language-independent format.
Python Node:
Laser Scanner
C++ Node : Map Building
Topic: “LaserData”
Publication
Subscription
Header header
Points32[] pointsXYZ
int32 numPoints
File-system level
Slides by Alec Poitzsch
Notes: (A) ROS implemented natively in each target langauge. (B) Language-independent Interface Definition Language (IDL) for defining messages:

## Slide 19: Lightweight
Encourages standalone libraries with no ROS dependencies:
Don’t put ROS dependencies in the core of your algorithm!
Use ROS only at the edges of your interconnected software modules: Downstream/Upstream interface
ROS re-uses code from a variety of projects:
  OpenCV : Computer Vision Library
  Point Cloud Library (PCL) : 3D Data Processing
  OpenRAVE : Motion Planning
Carnegie Mellon
ROS Community
Slides by Alec Poitzsch
Notes: Get downstream data, produce upstream data.
(A) Would like modules to be re-usable outside of ROS. Encourage all algorithm development to occur in standalone libraries w/ no dependencies on ROS. Don’t put ROS in your algorithm. (B) ROS re-uses code from a variety of projects: OpenCV, Point Cloud Library, OpenRAVE (ish). ROS just routing data in/out of respective software with as little wrapping as possible.

## Slide 20: Peer to Peer Messaging
No Central Server through which all messages are routed.
“Master” service run on 1 machine for name registration + lookup
Messaging Types:
  Topics : Asynchronous data streaming
  Parameter Server
Computation Graph
Slides by Alec Poitzsch
Notes: The ROS runtime "graph" is a peer-to-peer network of processes. No Central Server: Contrast w/ central-server-based Carmen: Consider the case of running robot w/ off-board compute-intensive tasks. If we run a central server offboard (or even onboard: go thru both cases) this results in unnecessary traffic across (slow) wireless link: many message routes are fully contained in subnets either onboard or offboard. Peer-to-peer connectivity avoid this issue Master : DNS / name service : register + find nodes. Nodes connect to other nodes directly; the Master only provides lookup information, much like a DNS server. Nodes that subscribe to a topic will request connections from nodes that publish that topic, and will establish that connection over an agreed upon connection protocol. The most common protocol used in a ROS is called TCPROS, which uses standard TCP/IP sockets. Styles of communication: *Asynchronous streaming of data over topics, and storage of data on a Parameter Server. 3rd type: synchronous RPC-style communication over services  we don’t really use

## Slide 21: Peer to Peer Messaging
Master: Lookup information, think DNS
roscore command  starts master, parameter server, logging
Publish: Will not block until receipt, messages get queued.
Delivery Guarantees: Specify a queue size for publishers: If publishing too quickly, will buffer a maximum of X messages before throwing away old ones
Transport Mechanism: TCPROS, uses TCP/IP
Bandwidth: Consider where your data’s going, and how
Slides by Alec Poitzsch
Notes: TCPROS is a transport layer for ROS Messages and Services. It uses standard TCP/IP sockets for transporting message data. Inbound connections are received via a TCP Server Socket with a header containing message data type and routing information.

## Slide 22: Free & Open Source
BSD License : Can develop commercial applications
Drivers (Kinect and others)
Perception, Planning, Control libraries
MIT ROS Packages : Kinect Demos, etc
Interfaces to other libraries: OpenCV, etc
Slides by Alec Poitzsch

## Slide 23: ROS Debugging
23
Shutdown “Object” node  re-compile  restart : won’t disturb system
Logging (VIDEO)
Kinect Driver
Object Recognition
Laser Scanner
Logger
Object Recognition
Logger Playback
Playback (VIDEO)
Slides by Alec Poitzsch
Notes: Editing Software: Say you want to debug 1 node in a large 20-node system. You can start all 20 nodes. Then if you want to change the 1 node you’re interested in: you can shut it down while leaving the other 19 running. You can re-code, re-compile, and re-launch that node. The ros infrastructure (graph / master name registration) will automatically adapt to nodes dropping out / activating. (B) Logging: Can dump any message stream to disk without modifying source code.
Logging/Playback: Recall your simulation environment in Labs

## Slide 24: Useful ROS Debugging Tools
rostopic: Display debug information about ROS topics: publishers, subscribers, publishing rate, and message content.
rostopic echo [topic name]  prints messages to console
rostopic list  prints active topics
… (several more commands)
rxplot : Plot data from one or more ROS topic fields using matplotlib.
rxplot /turtle1/pose/x,/turtle1/pose/y  graph data from 2 topics in 1 plot
Slides by Alec Poitzsch
Notes: Rxplot: Rotation angle of the wheels/ Encoder reading
Rostopic: What if you don’t know if your encoders are being read correctly, or if your motor died ( how does the robot know it is not responding )
DEBUGGING tools

## Slide 25: Useful ROS Debugging Tools
rxgraph
Slides by Alec Poitzsch

## Slide 26: ROS Visualization
Visualize:
Sensor data
Robot joint states
Coordinate frames
Maps being built
Debugging 3D markers
    VIDEO
Slides by Alec Poitzsch
Notes: (A) rviz (demo): tap into any message stream and visualize (if plugin available) Demo will show visualization of point clouds, robot joint states, coordinate frames, user-added markers

## Slide 27: Packages
Perception
  Point Cloud Library (PCL)
  OpenCV
  Kinect/OpenNI
Slides by Alec Poitzsch

## Slide 28: Back to Example: Launch files
roslaunch ardrone_tutorials keyboard_controller_with_tags.launch
ardrone_autonomy\src\ardrone_driver.cpp
ardrone_tutorials\src\keyboard_controller.py

## Slide 29: Example
ardrone_tutorials\src\keyboard_controller.py

## Slide 30: Example
ardrone_tutorials\src\drone_controller.py

## Slide 31: Example
Making modifications to the keyboard_controller.py file makes for a simple way to implement custom behaviors
Here we show some imports

## Slide 32: Example
Here we see our definitions for specific behaviors.
Here you can see our two behaviors on our chosen keys (feel free to choose your own)
ardrone_tutorials\src\keyboard_controller.py

## Slide 33: Example
Here we insert the first of our vision processing code.

## Slide 34: Example
Now we start to develop behaviors and bounds for that behavior

## Slide 35: Example
Now we use the key depress/release states to exhibit our wanted behavior (this is the depress code)

## Slide 36: Example
Now we modify the key release section of code

## Slide 37: Example
Now we can test the behaviors 

## Slide 38: Example
This is the OpenCV image processing portion of the code, brushed over this earlier.

## Slide 39: OpenCV
OpenCV is a great resource for manipulating images. We leave it open to you to decide what you would like to create!

## Slide 40: Some Ideas…
Easy: Proportional-Integral-Derivative (PID) controller: Smoother motion

## Slide 41: Some Ideas…
Easy: Proportional-Integral-Derivative (PID) controller: Smoother motion
Medium: OpenCV Person Detection + Following
http://www.pyimagesearch.com/2015/11/16/hog-detectmultiscale-parameters-explained/

## Slide 42: Some Ideas…
Easy: Proportional-Integral-Derivative (PID) controller: Smoother motion
Medium: OpenCV Person Detection + Following
Hard:
  Your own color histogram (e.g. hand) detector
  Deep-Learning Based Object Detection & Following
  Visual odometry: Re-trace steps after piloting

## Slide 43: In Closing
Please see me for the download of the python file that we made modifications to.
Be careful: Test code gently (low velocities or just debug outputs without action first!)
  Have a safety person watching it besides pilot!
Best of luck to all the teams!
Thanks to everyone involved in the AE Hackathon for hosting this fantastic event!!